## Slide 1: Reducing slurry temperature to lower NH3, N2O and CH4 emissions from pig fattening housing
Nadine Guingand (*), Yvonnick Rousselière Johan Thomas, Aurélien Collin
Ifip – institut du Porc
A study of the TEMPORALIS project supported by the French ecological transition Agency (ADEME)

## Slide 2: Context
Chart: 
| Pig
NH3 | 0.08
N2O | 0.07
CH4 | 0.09
NH3
CH4
N2O
Contribution of the pig sector
(Citepa, 2022)
NH3 : - 13% GHG : -20 %
France’s committements
IMPLEMENTATION OF TECHNIQUES FOR THE REDUCTION OF GASEOUS EMISSIONS
? Effectiveness, applicability
Notes: At the european level, France is committed to reducing its emission of ammonia by 13% and its emission of GHG by 20% by 2030 compared to 2005 emission. In France, in 2022, pigs are responsible of 8% for ammonia, 7% for nitrous oxide and 9% for methane at the national level, according to Citepa who is the french organization in charge of inventories
Meeting these commitments requires the implementation of reduction techniques in our livestock farms.

## Slide 3: Manure cooling – the principle
Reduction of the slurry temperature by captation of calories
Evaporator
Condenser
Heating/tapwater
Circuit of pipes installed in the prepit
Captation of calories by the heat transfer fluid circulating in the circuit of pipes
Notes: The principle is relatively simple and based on the captation of calories present in the slurry. Those calories can be used for heating or preheating water or air. A circuit of pipes filled with a heat transfer fluid is installed in the prepit and allows the recovery of calories from the slurry.

## Slide 4: Experimental design
MCSb room
MCSf room
Reference room
54
30 to 118 kg
Fully slatted floor
Slurry storage
Diffuse ceiling and under-floor extraction
Conventional setpoint temperature (22°C)
Multiphase dietary strategy
Notes: Three rooms with the same design were implicated in our study

## Slide 5: Experimental design
MCSPB room
MCSf room
Reference room
30- meter circuit of pipes
Fixed directly on the pit bottom
Filled with a heat transfer fluid (33% glycol)
Pit Bottom
20 W.m-2
MCSPB : Manure Cooling System – Pit Bottom

## Slide 6: Experimental design
MCSPB room
MCSF room
Reference room
Pit Bottom
Floating System
Raft floating on the surface of the slurry
2 consecutive batches between May to December
Same technical design than MCSPB
MCSFS : Manure Cooling System – Floating System

## Slide 7: Measurements and recordings
Zootechnical aspect
PIG WEIGHING
Entry, feed transition and slaughter + carcass data
FEED WEIGHING
Every day

## Slide 8: Measurements and recordings
Environmental aspect
PIG WEIGHING
Entry, feed transition and slaughter + carcass data
FEED WEIGHING
Every day
SLURRY
Height every 2 weeks -> volume
Sampling : feed transition + slaughter
GAS (NH3, N2O, CH4)
Ambient air - Every 3 minutes

## Slide 9: Measurements and recordings
Ambience
PIG WEIGHING
Entry, feeding transition and slaughter+ carcass data
FEEDING WEIGHING
Every day
SLURRY
Height every two weeks -> volume
Sampling : feed transition + slaughter
GAS (NH3, N2O, CH4)
Ambient air – every 3 minutes
TEMPERATURE (Ambience and Slurry) VENTILATION RATE
Every 15 minutes

## Slide 10: Results – zootechnical performance
FCR kg.kg-1
2,56±0,2 a
2,50±0,1 a
2,50±0,1 a
2,75
Meat lean
60,9±2,2 a
61,3±2,0 a
60,9±1,9 a
60,7
ADG g.d-1
917±186 b
954±103 a
932±91 ab
803
National Value
(a,b) : Values accompanied by different letters on the same line indicate a statistically significant difference at the 5% level

## Slide 11: Ambience – Temperature in the air
Average values expressed in °C
26,5±1,9 (a)
Set point temperature 22°C
26,5±2,0 (a)
25,7±2,2 (b)
(a,b) : Values accompanied by different letters on the same line indicate a statistically significant difference at the 5% level
25,0±0,8 (a)
25,2±1,0 (a)
23,9±1,1 (b)
►Reduction of the ambient temperature for the MCSPB room
Air

## Slide 12: Ambience – Temperature of the slurry
Average values expressed in °C
Measures taken at the botton of the pit
23,7±0,8 (a)
Impact of ambient temperature on slurry (Guyot et al., 2022 – Guingand et al., 2024)
18,1±1,6 (b)
15,8±2,3 (c)
(a,b) : Values accompanied by different letters on the same line indicate a statistically significant difference at the 5% level
22,5±0,6 (a)
16,7±2,3 (b)
16,1±3,8 (c)
Slurry
Good efficiency of both MCS

## Slide 13: Environmental aspect – NH3
Average values expressed in kg N_NH3.place-1.year-1
2,3±1,3
2,5 – 3
Guingand et Courboulay, 2019 Philippe et al., 2011 Santonia et al., 2017
2,4±1,4
2,0±1,4
2,2±1,3
2,2±1,3
1,9±1,4

## Slide 14: Environmental aspect – NH3
Average values expressed in kg N_NH3.place-1.year-1
2,3±1,3
2,4±1,4
2,0±1,4
2,2±1,3
2,2±1,3
1,9±1,4
Reduction lower than 20% for the « Pit Bottom » System

## Slide 15: Environmental aspect – NH3
Average values expressed in kg N_NH3.place-1.year-1
2,3±1,3
2,4±1,4
2,0±1,4
2,2±1,3
2,2±1,3
1,9±1,4
No effect of the « Floating System »

## Slide 16: Environmental aspect – NH3
Average values expressed in kg N_NH3.place-1.year-1
2,3±1,3
Hansen et al., 2013 : relation between installed cooling capacity and ammonia reduction : 10 % per 10 W/m2
► In our study : 20 W/m2 –> 20 % - close to our result
2,4±1,4
2,0±1,4
2,2±1,3
2,2±1,3
1,9±1,4
Holm et al., 2016 : Reduction (%) =1,5 x – 0,008x2 with x = Cooling capacity in W/m2
► In our study : with 20W/m2 -> 26,8% - higher than our result

## Slide 17: Environmental aspect – N2O
Average values expressed in kg N_N2O.place-1.year-1
0,08±0,02
0,10 – 0,25
Philippe et al., 2015
IPCC, 2019
0,09±0,02
0,08±0,02
0,08±0,01
0,08±0,02
0,08±0,01
No effect of both MCS

## Slide 18: Environmental aspect – CH4
Average values expressed in kg C_CH4.place-1.year-1
8,5±0,1
2– 5
Philippe et al., 2011
IPCC, 2019
3,4±0,2
2,2±0,1
4,5±0,2
2,0±0,5
1,4±0,3

## Slide 19: Environmental aspect – CH4
Average values expressed in kg C_CH4.place-1.year-1
8,3±0,1
High efficiency of the Pit Bottom System (70%)
3,4±0,2
2,2±0,1
4,5±0,2
2,0±0,5
1,4±0,3

## Slide 20: Environmental aspect – CH4
Average values expressed in kg C_CH4.place-1.year-1
8,5±0,1
3,4±0,2
2,2±0,1
4,5±0,2
2,0±0,5
1,4±0,3
High efficiency of the Floating System (55%)

## Slide 21: Environmental aspect – CH4
Average values expressed in kg C_CH4.place-1.year-1
8,5±0,1
Reduction of the activity of methanogenic bacteria in the cold slurry
3,4±0,2
2,2±0,1
4,5±0,2
2,0±0,5
1,4±0,3

## Slide 22: Conclusions
Efficiency lower than expected on NH3…
20 W/m2
40 W/m2
Cette photo par Auteur inconnu est soumise à la licence CC BY-NC
Lower temperature on the area between slurry and slatted floor
Degradation of animal welfare
Consequences on performance?

## Slide 23: Conclusions
Efficiency lower than expected on NH3…
… but higher than expected on CH4
Cette photo par Auteur inconnu est soumise à la licence CC BY-NC
High interest in term of National Low-Carbon Strategy
Increased profit through energy recovery from slurry (not yet analyzed)
Implantation in existing building can be difficult (volume of the pit for the MCSPB – adaptation for the MCSF)
Expensive technique although the save of energy

## Slide 24: Conclusions
Cette photo par Auteur inconnu est soumise à la licence CC BY-NC
The MCSPB is easier to implement than the MCSF
Maintenance of the technique
Evolution of circuit porosity ? Risk of leaks ?.....
Especially in new buildings

## Slide 25
        nadine.guingand@ifip.asso.fr
            07 62 53 68 21
              IFIP – Pacé - France
This study is part of the project called TEMPORALIS * funded by ADEME
Thanks for your attention !
*Température en porcheries et réduction des émission d’ammoniac du lisier – 1962C0014